Specifications of 1/3” Sharp CCD（38603+2321）

| ITEM: | Specification |
| --- | --- |
| Configuration scheme: | 1/3” Sharp CCD（38603+2321） |
| Image Sensor: | 1/3” Sharp CCD |
| Effective Pixels: | PAL 500H×582V NTSC 510H×492V |
| TV System: | PAL/NTSC |
| Resolution: | 420TVL |
| Minimum Illumination: | 0Lux(Infrared lights on) 0.05Lux(day)/F1.2 |
| Signal to noise ratio: | ≥48dB |
| Video Output: | 1.0Vp-p/75Ω |
| Automatic gain control: | ON |
| Backlight compensation: | AUTO |
| Electronic shutter: | 1/50(1/60) - 1/100000 second |
| Gamma correction: | 0.45 |
| Working voltage: | DC12V±5% |
| Working temperature: | -20℃-60℃ RH95% Max |
| Storage temperature: | -30℃-80℃ RH95% Max |
| Lens: | 2.5mm/2.8mm/3.6mm (optional) |
| Microphone: | Optional |
| Output connector: | RCA(AV)/Aviation/S-Video/BNC (optional) |