Specifications of 1/3” SONY Super HAD CCD（639+4143）

| ITEM: | Specification |
| --- | --- |
| Configuration scheme: | 1/3” SONY Super HAD CCD（639+4143） |
| Image Sensor: | 1/3” SONY CCD |
| Effective Pixels: | PAL 752H×582V NTSC 768H×494V |
| TV System: | PAL/NTSC |
| Resolution: | 600TVL |
| Minimum Illumination: | 0.01Lux |
| Signal to noise ratio: | ≥50dB |
| Video Output: | 1.0Vp-p/75Ω |
| Exposure mode: | electronic exposure |
| Electronic shutter: | 1/50(1/60) - 1/100000 second |
| Gamma correction: | 0.45 |
| Working voltage: | DC12V±5%(DC12-24V Optional) |
| Working temperature: | -20℃-60℃ RH95% Max |
| Storage temperature: | -30℃-80℃ RH95% Max |
| Lens: | 2.8mm (optional) |
| Microphone: | NO (Optional) |
| Output connector: | RCA(AV)/Aviation/S-Video/BNC (optional) |
| IR Distance : | 15m |